Refer to clinical criteria for bathroom and toilet modifications and ensure eligibility before proceeding with prescription

Client name:      	Client file no:

Client address:

Telephone No:

Prescriber name:      	Prescriber agency/team/site:

# Building type:	Solid brick	                Brick veneer	         Timber frame

# Age of House:      	 years

# BATHROOM/TOILET

# Layout

Change Bathroom Layout (attach diagram)

# Walls

Remove wall/section of wall to increase size/circulation space of bathroom

Remove wall to combine existing toilet and bathroom

# Doorway

Widen doorway and supply and install new door

Door size:      	mm x       	mm

Door type:

Reuse existing door handles   New Door handles

Type:

# Shower/bath

Remove shower hob and shower screen

Remove bath and modify plumbing

Shower recess: regrade floor with no step down to shower

Supply and install hand held shower: Require 1.5m tiled shower area if achievable, for tiling within shower alcove from either side of fixed plumbing outlet (refer to bathroom electrical safety procedure)

Reuse existing tap ware 	                Supply and install new tap ware:

Type:

Supply and install new shower curtain rail

Supply and install shower seat fixed to wall/floor

Supply and install grab rails in accordance with AS1428.1 Diameter 32 mm standard, Distance between inner edge of handrail and wall or other obstruction no less than 45mm. Rail securely fixed to stud or noggin in timber wall or into masonry concrete or concrete wall.            See attached diagram

Quantity:      	Locations:

Length:      	mm	Height from floor:      	mm

Length:      	mm	Height from floor:      	mm

Home Modification Specification Form – Bathroom / Toilet

# Hand basin/vanity

Relocate existing hand basin and vanity		Supply and install new hand basin

Supply and install new shelf		See attached diagram

Relocate existing mirror		See attached diagram. Location:

# Reuse existing tap ware 		Supply and install new tap ware

# Type:

# Toilet

Supply and install new toilet	               Standard toilet	                   Non standard toilet

Supply and install new cistern

Relocate existing toilet roll holder		Supply new toilet roll holder.

Supply and install grab rails in accordance with AS1428.1  Diameter 30mm-50mm, Distance between inner edge of handrail and wall or other obstruction no less than 45mm. Rail securely fixed to stud or noggin in timber wall or into masonry concrete or concrete wall.           See attached diagram

Quantity:      	Locations:

Length:      	mm	Height from floor:      	mm

Length:      	mm	Height from floor:      	mm

# Lights/power

Relocate light switch		See attached diagram

Relocate light		See attached diagram

Relocate power outlet (refer to bathroom electrical safety procedure)

# Tiling/painting floors/walls

Tile within shower recess to      	metres (2 metres max)

Tile walls to      	mm (minimum to meet building requirements)

# 2 rows of tiles over hand basin

1 row of skirt tiles

Make good floor tiles to bath where removed

Make good tiling to walls

Treat floor with slip resistant treatment

Make good painting to walls and ceiling

Other details:

Clinical reasoning if deviating from AS1428.1(2009), please remember to write these in the clients casenotes:

Home Modification Specification Form – Bathroom / Toilet

Please complete signed diagram with measurements below

Agreed Modifications Diagram

Client name:

- Include all dimensions in mm

- Include all relevant fixtures, (eg grab rails, light switch, power points, basin, cistern, soap holder, toilet paper dispenser, taps, shower hose, wall studs, etc.)

- Refer to bathroom modifications prescriber notes

I agree to the home modifications being completed to the above specifications

Client’s signature:	Date:

Property owner’s signature:	Date:

Prescriber’s signature: __________________________________________Date:

# Text boxes

Domiciliary Equipment Service

Home Modification Specification Form Bathroom / Toilet

Check for latest e-version as printed copies may be out of date: Released 17/5/2013

Phone: 1300 295 786         Fax: 1300 295 839          Email: equipment.feedback@dcsi.sa.gov.au            Page 2 of 3

Check for latest e-version as printed copies may be out of date: Released 17/5/2013

Phone: 1300 295 786	     Fax: 1300 295 839       Email: equipment.feedback@dcsi.sa.gov.au	     Page 3 of 3

Check for latest e-version as printed copies may be out of date: Released 17/5/2013

Phone: 1300 295 786	    Fax: 1300 295 839        Email: equipment.feedback@dcsi.sa.gov.au         Page 1 of 3