Refer to “Specific eligibility criteria Long Ramps” and ensure eligibility before proceeding with prescription

Client name:      	Client file no:

Client address:

Telephone no:

Prescriber name:      	Prescriber agency/team/site:

# Building type:         Solid brick         Brick veneer          Timber frame

# Age of House:      	 years

Ramp Location:     Front                  Rear                       Other

# RAMP

Supply and install new ramp

Location:	 Front                  Rear                        Side

Demolish:	 Existing steps    Existing pathways   Other

# Dimensions

# See attached diagram

Total height      	mm (1000mm max)

Length      	mm                    Gradient 1:14          Other gradient

Unobstructed width                        1000mm                  Other      	  mm

Camber/cross fall maximum 1:40

# Ramp Material

Concrete

Timber

Note: Refer to Ramp Prescriber Notes in regards to selecting ramp material

# Landings

Install top landing:      	mm x       	mm	             Aligned with doorsill	 See attached diagram

Install bottom landing:      	mm x       	mm	 See attached diagram

Install other landing:      	mm x      	mm	 See attached diagram

# Kerb/kerb rail

Install kerb/kerb rail      	mm high with top of kerb/kerb rail between 65 - 75mm or >150mm above surface

of ramp (i.e. not between 75mm – 150mm high). Kerb rail within 100mm of side of ramp.

# Home modification specification form                      Long ramp

# Handrails

Install top handrail(s) at      	 mm high (865-1000mm)	50mm clearance from adjacent wall

Install middle handrails at      	mm high	50mm clearance from adjacent wall

Handrail to surround top landing

Handrail to extend 300mmm beyond ramp at	 bottom	 top

Handrail diameter 30-50mm with 270 degree uppermost surface obstruction free

# Paths

Repair existing path to ramp: type of path (e.g. concrete, paving)

Install path to ramp: 	length      	mm x width	1000mm	 Other      	mm

See diagram attached.

# Plumbing

Relocate garden tap

Relocate gully trap

Provide access to gully trap

Other details:

Clinical reasoning if deviating from AS1428.1(2009), please remember to write these in the clients casenotes:

Home modification specification form                      Long ramp

Please complete signed diagram with measurements below

Agreed Modifications Diagram

Client name:

- Include all dimensions in mm

- Refer to ramp prescriber notes

I agree to the home modifications being completed to the above specifications

Client’s signature:	Date:

Property owner’s signature:	Date:

Prescriber’s signature:	Date:

# Text boxes

Domiciliary Equipment Service

Home modification Specification form Long ramp

Check for latest e-version as printed copies may be out of date: Released 17/5/2013

Phone: 1300 295 786      Fax: 1300 295 839     Email: equipment.feedback@dcsi.sa.gov.au                 Page 1 of 3

Check for latest e-version as printed copies may be out of date: Released 17/5/2013

Phone: 1300 295 786	Fax: 1300 295 839     Email: equipment.feedback@dcsi.sa.gov.au 	   Page 2 of 3

Check for latest e-version as printed copies may be out of date: Released 17/5/2013

Phone: 1300 295 786	  Fax: 1300 295 839        Email: equipment.feedback@dcsi.sa.gov.au 	        Page 3 of 3